## Slide 1
Lower Platte Missouri Tributaries Model
Hydrologic Connection Analysis
Lower Platte Basin Tech Committee Meeting
March 4, 2019
Philip Paitz
Water Planning IWM Analyst

## Slide 2
Lower Platte Missouri Tributaries (LPMT) Model Construction Timeline
LPMT Model Construction Domain and Boundaries
Cycle Well Analysis
Cycle Well Zones
Results – All Zones, Missouri Tributary Zones, and a Single Zone
Outline

## Slide 3
Provide a regional numerical groundwater model to aid in the study of the impact of pumping on streams in the area
Before the development of the LPMT model there was no regional model encompassing the eastern region of Nebraska. The LPMT model covers the northern and central part of that region
Region contains complex hydrogeologic features which range from the High Plains Aquifer in the western side, to alluvial aquifers near the major streams, and local perched and semi-perched aquifers in regions containing glacial till
Why Was the LPMT Model Constructed?

## Slide 4
Three HDR reports from 2012, 2013, and 2014 provided the basis for the development of the model
Initial model work started in July of 2014. Model development was contracted out to HDR
First version of the model was finished late 2016 and was reviewed by Olsson Associates. Revisions requested included separating the evapotranspiration from the watershed model to an EVT package, incorporating pilot points, and modify the zonation constraints
Final model incorporating revisions from the review was finished December of 2018
LPMT Model Construction Timeline

## Slide 5
Layers
  Model contains two layers where Layer 1 represents the principle aquifer and Layer 2 represents various bedrock aquifer units
Grid
  Consists of 350 Rows and 282 Columns of ½ Mile by ½ Mile cells
  64,347 active cells in Layer 1
  69,168 active cells in Layer 2
Stress Periods – January 1960 through December 2013
  1 Steady State, 26 Transient Annual, 336 Transient Monthly
Packages
  Well, Recharge, Stream Flow Routing, River, and Evapotranspiration
LPMT Model Construction Domain and Boundaries

## Slide 6
LPMT Model Construction Domain and Boundaries

## Slide 7
Cycle Well Analysis
Natural Condition
Induced Infiltration
Capture

## Slide 8
In order to calculate Stream Depletion Factors a cycle of pumping of a known, fixed quantity for every stress period by a fictional well is needed
This process is repeated for every cell in a model’s active domain
Cycle Well Analysis
is the cumulative stream leakage after the new well
is the cumulative stream leakage of the baseline
is the total pumping from the new well

## Slide 9
Cycle Well Analysis
is the cumulative stream leakage after the new well
is the cumulative stream leakage of the baseline
is the total pumping from the new well

## Slide 10
Hydrologic connectivity determined by running a fifty year simulation
LPMT cycle well analysis consists of original models 336 transient monthly stress periods plus the last 132 repeated twice
  Original 336 transient periods – Jan 1986 to Dec 2013
  Repeated last 127 periods twice - Jan 2002 to Dec 2013
  Total of 600 stress period representing fifty years
All model packages were modified to represent the stress period changes
LPMT Cycle Well Setup

## Slide 11
Zones were created to aid in the analysis of hydrologically connected areas
The zones are based off of HUC 10 Watershed boundaries and are the same for both layers
Missouri, Blue, Loup, and Platte Tributaries were grouped
Bazille and Elkhorn watersheds without stream cells were grouped
Total of fifty nine zones
LPMT Cycle Well Zones

## Slide 12
LPMT Cycle Well Zones

## Slide 13
LPMT Cycle Well Results 1
All Zones

## Slide 14
LPMT Cycle Well Results 2
Missouri Tributary Zones

## Slide 15
LPMT Cycle Well Results 3
Single Tributary Zone

## Slide 16
Finish post-processing the cycle well results
QAQC the process, post-processing, and results
Export results to shapefiles and create final csv files for each zone
Finalize documentation and write metadata for shapefiles
Distribute results to public
Also ahead with the NRD’s help
  Examine and incorporate AEM data into the LPMT Model
  Develop local sub-models
What’s Left to Do?

## Slide 17
LPMT Model was constructed to aid in the study of impact to streams within the region with an emphasis on hydrologic connectivity
Cycle well analysis was conducted using the LPMT Model expanded to fifty years
Zones allow for hydrologic connectivity to analyzed at watershed level
Post-processing and QAQC need to be completed
Summary

## Slide 18
Philip Paitz
Water Planning IWM Analyst
philip.paitz@nebraska.gov