## Slide 1
Lower Platte Missouri Tributaries Model
NRD Spring Water Conference
March 4, 2019
Philip Paitz
Water Planning IWM Analyst

## Slide 2
Lower Platte Missouri Tributaries (LPMT) Model Construction Timeline
LPMT Model Construction Domain and Boundaries
Discussion of Model Packages
Calibration and Sensitivity Analysis
Results –Missouri Tributary Zones and a Single Zone
Outline

## Slide 3
Provide a regional numerical groundwater model to aid in the study of the impact of pumping on streams in the area
Before the development of the LPMT model there was no regional model encompassing the eastern region of Nebraska. The LPMT model covers the northern and central part of that region
Region contains complex hydrogeologic features which range from the High Plains Aquifer in the western side, to alluvial aquifers near the major streams, and local perched and semi-perched aquifers in regions containing glacial till
Why Was the LPMT Model Constructed?

## Slide 4
Three HDR reports from 2012, 2013, and 2014 provided the basis for the development of the model
Initial model work started in July of 2014. Model development was contracted out to HDR
First version of the model was finished late 2016 and was reviewed by Olsson Associates. Revisions requested included separating the evapotranspiration from the watershed model to an EVT package, incorporating pilot points, and modifing the zonation constraints
Final model incorporating revisions from the review was finished December of 2018
LPMT Model Construction Timeline

## Slide 5
Layers
  Model contains two layers where Layer 1 represents the principle aquifer and Layer 2 represents various bedrock aquifer units
Grid
  Consists of 350 Rows and 282 Columns
  ½ Mile by ½ Mile cells
  64,347 active cells in Layer 1
  69,168 active cells in Layer 2
Stress Periods – January 1960 through December 2013
  1 Steady State, 26 Transient Annual, 336 Transient Monthly
Packages
  Well, Recharge, Stream Flow Routing, River, and Evapotranspiration
LPMT Model Construction Domain and Boundaries

## Slide 6
LPMT Model Construction Domain and Boundaries

## Slide 7
Streams
Represented internally by the Stream Flow Routing Package (SFR)
Cells containing perennial streams were selected to be stream cells
Baseflow of streams entering the model domain were calculated at gaging stations to aid water budget
SFR allows for stream drying and rewetting as well as creating a water budget term for calculating aquifer/stream exchange

## Slide 8
Streams

## Slide 9
Watershed Model Outputs
Four major components to the Watershed Model
Climate model
  Uses precipitation, temperature, and reference ET to generate inputs for the regionalized soil water balance model
Soil water balance model – CROPSIM
  Uses climate model data, soil data, and cropping information to generate the net irrigation requirement
Spatial and temporal distribution of CROPSIM results
Regionalized soil water balance model
  Develops recharge and pumping estimates based on CROPSIM results
Output Well and Recharge packages for the groundwater model

## Slide 10
Watershed Model Outputs - Wells

## Slide 11
Watershed Model Outputs - Recharge

## Slide 12
Evapotranspiration
Added to the model post-review
EVT is represented in areas where the water table is near the surface
Uniform extinction depth of 7 feet was used
Maximum ET rate of 40 in/yr, which was reduced by the average dryland pasture ET to account for water being taken out by the watershed model

## Slide 13
Evapotranspiration - EVT

## Slide 14
Hydrogeologic Parameters
Hydraulic Conductivity
  Derived from inverse parameter estimation utilizing pilot points and K zones
  Calculated with 26 conductivity zones and 309 pilot points
  K Zones based on test-hole data, well data, aquifer absent areas, glacial till regions, and the 30 meter USGS DEM
Storage
  Layer 1 represented by unconfined specific yield term (0.15)
  Layer 2 represented by a confined specific storage term (0.01)
Leakance
  Effective vertical hydraulic conductivity between the model layers
  Calculated through inverse parameter estimation similar to hydraulic conductivity. Three zones were used

## Slide 15
Hydraulic Conductivity

## Slide 16
Hydraulic Conductivity

## Slide 17
Calibration
Calibration Targets
  Groundwater Levels
  Stream Baseflow
  Synoptic Seepage
Calibration Parameters
  Recharge
  Hydraulic Conductivity
  Storage
  Leakance
Water Budget

## Slide 18
Groundwater Levels
Set of 1080 wells containing 83,575 measurements were used to represent the calibration period
  Only wells spanning at least 10 years worth of data and 10 measurements during the calibration period were used
  June, July, and August measurements were removed to limit impact from pumping
  Only one monitoring well per cell was used to limit bias
2010 potentiometric surface was used as a target

## Slide 19
Groundwater Levels

## Slide 20
Stream Baseflow
40 streamflow gaging stations were chosen as calibration targets
Baseflow separation was conducted on the daily total streamflow hydrographs as the groundwater model can only simulate baseflow
The reach gains of the streams throughout the model helped in understanding how baseflow was being generated by the model

## Slide 21
Stream Baseflow

## Slide 22
Synoptic Seepage
A survey of 90 known or suspected seepage locations was conducted by NeDNR in October 2014
  Goal was to identify seepage areas
  Used to see if the groundwater model could reproduce them
67 of the sites visited were noted as “wet”
  Model was able to replicate 27
Some of the suspected sites were dubious as there had been recent rainfall event prior to the site visit
  Ponding
  Overland flow

## Slide 23
Synoptic Seepage

## Slide 24
Water Budget

## Slide 25
Sensitivity Analysis

## Slide 26
The LPMT Model in Use
The Lower Platte Missouri Tributaries Model is now being used within the department to determine the hydrologically connected areas within the region
Currently being incorporated into SUSTAIN and the CIR calculator
In partnership with the NRDs, there are currently two pilot projects underway
  Examine and incorporate AEM data into the LPMT Model
  Develop local sub-models

## Slide 27
LPMT Cycle Well Results 1
Missouri Tributary Zones

## Slide 28
LPMT Cycle Well Results 2
Single Tributary Zone

## Slide 29
LPMT Model was constructed to aid in the study of impact to streams within the region with an emphasis on hydrologic connectivity
Utilizes a Watershed model to simulate pumping and recharge
Model was calibrated to three targets
  Groundwater Levels
  Stream Baseflow
  Synoptic Seepage
Process is underway to determine the hydrologically connected areas within the model
Summary

## Slide 30
https://dnr.nebraska.gov/Lower-Platte-Missouri-Tributaries-Groundwater-Model
Where Can I Get the LPMT Model?

## Slide 31
Philip Paitz
Water Planning IWM Analyst
philip.paitz@nebraska.gov

## Slide 32
SUSTAIN and the Lower Platte Missouri Tributaries Model
NRD Spring Water Conference
March 4, 2019
Margeaux Carter
Water Planning IWM Specialist

## Slide 33: SUSTAIN: A Water Management Tool
Software tool developed by NeDNR for NRDs and water managers
Improve access to
  Regional historical water use data
  NeDNR’s hydrologic model outputs
Increase transparency of NeDNR’s
  Hydrologic modeling process
  Water management project evaluation methods
Increase understanding of
  Changing water use patterns
  Impacts of water use on regional hydrologic systems

## Slide 34: SUSTAIN: A Water Management Tool
A graphical user interface which allows NRDs to:
Access NeDNR data
View groundwater model inputs
Evaluate water management scenarios
Run NeDNR groundwater models
Customize graphs
Export data

## Slide 35: SUSTAIN: A Water Management Tool
Access water use data
  model-wide data
    UNW and LPMT models
    1960 - 2010
    Includes water use reporting meter data
  easily process and display data for education/outreach
  export data for more options
Evaluate water management projects
  Estimate likely to be similar NeDNR’s official evaluation
  Good for tuning project proposal
  NeDNR support in development

## Slide 36
LPMT Model
UNW Model